16 bit TTL CPU

Machine word
-always one nibble of opcode bits and the second nibble includes which registers are involved
-the next byte can be an immediate value.
-data-bus is 8 bits wide
-address-bus is 15 bits wide: 0x0000 to 0x7FFF is the ram, 0x8000 to 0xFFFF is the flash!
-thus we have 32kb flash and 32kb ram. We can execute both from ram and flash
-To adress something larger than 8-bit addresses, the DR(DR) is used for the bits 7..15: For STR and LDR
-PC is 16 bits wide: PC_L:0...7; PC_H:8...15
-ALU is 8 bits wide
-32kb Stack FIFO. The stack memory can only be addressed via PUSH and POP. The stack memory is can not be addressed via normal registers since it is not connected to the address-bus. Thus we have a total of 32kb Ram +3 2KB Stack = 64kb RAM and 32kb ROM.

I/O
IN and OUT instructions are used to access input and output ports. They are also used to read from and write to the SREG register.

Memory
Ram(w24129ak12) and Flash(W29EE011) is connected to the same address Bus. The memory devices have both three-states outputs. The bank register controls with the highest bit(bit14 on the address bus) whether RAM or the flash will be targeted. Writing to the flash will not work since a whole page(256bits) needs to be written at once. Maybe I can upgrade this later with a more decent flash chip, which will allow easy writing just like the ram.

Instructions
Instruction Nibble 1
Nibble 1	Instruction	Note	Nr. Of cycles	Cad Designed	Notes	Argument type: indicates which table is used to decode the arguments
0x0	ADD reg1, reg2	reg1+ reg2. result is in reg1		Yes	Always with carry. Clear carry with add reg1, 0 before if needed	0
0x1	SUB reg1, reg2	reg1-reg2. Result is in reg1		Yes	To be tested!	0
0x2	NOR reg1, reg2	Logic NOR. Result in reg1		Yes		0
0x3	AND reg1, reg2	Logic AND. Result in reg1		Yes		0
0x4	MOV reg1,reg2	Mov reg2 int reg1. Reg2 can be a number!		Yes		0
0x5	MOVZ reg1, reg2	Same as mov. executes only when reg1 is zero		Yes	Do we need a flipflop for REG1_ZERO_MOVZ, if reg1 is changed during a MOVZ instruction, which in turn could have an effect on the STATE_SIGNAL of the / MOV instruction??	0
0x6	JMP reg1, reg2 / JMP reg1	Far jump(needed for jumps over the 256b borders) reg1 is LOW byte, reg2 HIGH byte, reg2 can be a nr / JMP can be used with a single argument as well. Its the same as JMP reg1, PC_HIGH		No	If the JMP has only one argument, it is used as an offset instead as an address.	0
0x7	JMPZ reg1	ADD the signed offset reg2 to PC if Reg1 is not zero		Yes	Can jump maximal 127 bytes! / Use JMP instead!	1
0x8	JMPC reg2	Add the signed offset reg2 to PC if carry is set		No		1
0x9	STR reg1, [reg2]	Store reg1 at *reg2. Reg2 can be a number		Yes		0
0xA	LDA reg1, [reg2]	Load value pointed to by reg2(or number)		Yes		0
0xB	SET_DR reg1	Set the DataRegister to reg1		Yes		1
0xC	IO reg1, PORTA / IO PORTA, reg1	Read Input PORTA into reg1 / Output reg1 on PORTA		No	Only work with reg1 and reg2	2
0xD	INC_PTR reg1, reg2	Increment the register set (reg1&DR) by reg2,		No		0
0xE	PUSH reg1	Simple fifo in seperated Memory		No->TODO, OLD implementation		1
0xF	POP reg1	Simple FIFO in seperated Memory		No->TODO, OLD implementation		1

The second instruction Nibble decides which registers are used in the instruction defined in the first nibble.
Instruction Nibble 2

Argument decode Table 0

Opcode Nibble 2	Involved Registers(all Instructions except MOVN)
0x0	Reg1,number
0x1	Reg2, number
0x2	Reg3, number
0x3	Reg4, number	// JMP(Z/C) uses this operand byte to encode JMP(Z/C) NUMBER, thus JMP(Z/C) reg4, NUMBER cant be used.
0x4	Reg1, reg2
0x5	Reg1, reg3
0x6	Reg1, reg4
0x7	Reg2, reg1
0x8	Reg2, reg3
0x9	Reg2, reg4
0xA	Reg3, reg1
0xB	Reg3, reg2
0xC	Reg3, reg4
0xD	Reg4, reg1
0xE	Reg4, Reg2
0xF	Reg4, Reg3

Argument decode Table 1

Used for all commands which only have one argument like JMPC, JMPNZ, POP, PUSH.

Opcode Nibble 2	Involved Registers(all Instructions except MOVN)
0x0	Number
0x1	Reg1
0x2	Reg2
0x3	Reg3
0x4	Reg4
0x5	PC
0x6	DR
0x7	Unused
0x8	Unused
0x9	Unused
0xA	Unused
0xB	Unused
0xC	Unused
0xD	Unused
0xE	Unused
0xF	Unused

Argument decode Table 2

Used by the IN and OUT instructions

Opcode Nibble 2	Involved Registers(all Instructions except MOVN)
0x0	Reg1, PORTA
0x1	Reg1, PORTB
0x2	Reg1, PORTC
0x3	Reg1, PORTD
0x4	Reg2, PORTA
0x5	Reg2, PORTB
0x6	Reg2, PORTC
0x7	Reg2, PORTD
0x8	PORTA, Reg1
0x9	PORTB, Reg2
0xA	PORTC, Reg3
0xB	PORTD, Reg4
0xC	PORTA, Reg1
0xD	PORTB, Reg2
0xE	PORTC, Reg3
0xF	PORTD, Reg4

The Status Register
The SREG register consists of two 8-bit registers. Register A and register B.
Register A:
Register	Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
A								Carry
B

The Status Registers can be retrieved via the Port command.
SREG reg1, reg2 ; retrieves SREG_A into reg1 and SREG_B into reg2 //CHANGED!

Current Problems
ALU carry_out signal is changed by NOR and AND instructions. Need a flip Flop or something similar

In order to increment the 16bit registers, two add instructions need to be done. First the lower 8bits are added, and then the higher 8bits with the carry-bit of the first calculation:
ADD r1_l, r2_l	//add without carry(or just with deleted carry)
ADC r1_h, r2_h	//add with carry(may be 1 or 0)

Current State
Module	Status	Notes
ALU	Done	Need FlipFlop for Carry out bit
Decoder	Todo
Memory	Todo
Registers	Todo

Candidates for the reserved Instruction
-INC_PTR ;increases the ptr pair BR, reg1 by 1. BR is high byte, reg1 low. This simplifies addressing arrays and other data structures.
-Some other instruction, which simplifies accessing memory by not being constroined by the 256bytes barrier... We need 16bit pointers!
-Or just and ADD without carry. This is easy to implement and removes potential errors and bugs from the code. It removes complexity!

PROBLEMS
Startup
RING_CNTR_CLR needs to go high -> this clears the Ring Counter. Is this signal low active?
Further investigation is needed!
CLR_ALL_REGS_NOT needs to go low for a short period and then for the rest of the time HIGH
Memory Access
-Read: can we apply the address, clear_not_oe and clear_not_cs in one istruction and fill the registers in the following instruction? 2Cycle Memory Access would be possible with this!

Adressing Memory
Step	Read	Write
1	Apply address to A-bus, clear Not_OE and NOT_CS	Apply address to A-bus, Apply data to D-bus, clear Not_OE and NOT_CS
2	wait > 6nS	wait > 6nS
3	Read Data from Databus / Write read data back to registers	Set NotCS
4	Set NotCS

Fetch and Decode
Step	Fetch and Decode
1	Connect PC to Mem Addr, IR to DBus
2	Do Mem Read and IR write Signals
3	Connect PC and 1(through multiplexer ctrl)to ALU, ADD ctrl
4	Reg write back

Decoder and Execution steps
Cycle	ALU	MOV	DR	LDA	STR	IN	OUT	PUSH	POP	FAR_JUMP
1	REGS->DBus / Apply ALU selection	Write REG to DBus	Write REG to DBus			Connect PORT-reg to DBus	Connect REG to DBus
2	Latch ALU output(becaus src and dest may be the same)	Fill REGs	Fill DR			Fill REG	Fill PORT-reg
3	Fill REG
4
5
6
7

Calling Convention
-Caller saves his working registers(For example on the stack)
-Arguments are passed in Reg1, Reg2, Reg3, Reg4. Additional arguments are passed via the stack
-Return Address is passed through the stack. First the Low byte is pushed, than the High byte
-Return values are in Reg1 and Reg2. Additional return values are on the stack (Reg3 and 4 cannot be used since they are needed for the return JMP instruction)