16 bit TTL CPU
Machine word
-always one nibble of opcode bits and the second nibble includes which registers are involved
-the next byte can be an immediate value.
-data-bus is 8 bits wide
-address-bus is 15 bits wide: 0x0000 to 0x7FFF is the ram, 0x8000 to 0xFFFF is the flash!
-thus we have 32kb flash and 32kb ram. We can execute both from ram and flash
-To adress something larger than 8-bit addresses, the BankRegister(BR) is used for the bits 7..15. Affected instructions: STR and LDA
-PC is 16 bits wide: PC_L:0...7; PC_H:8...15
-ALU is 8 bits wide

Stack
-32kb Stack FIFO. The stack memory can only be addressed via PUSH and POP. No stack pointer arithmetic is possible because the stack is not connected to the address-bus. Thus we have a total of 32kb Ram +32KB Stack = 64kb RAM and 32kb ROM.
The Stack pointer is implemented using 74xx193 binary counter chips.

I/O
I/O can be written to with the pop/ldr and read from with the push/str instructions. There are 2 Output ports and one input port. Always 8 bits wide.

Memory
Ram(w24129ak12) and Flash(W29EE011) is connected to the same address Bus. The memory devices have both three-states outputs. The bank register(BR) controls with the highest bit(bit14 on the address bus) whether RAM or the flash will be targeted. Writing to the flash will not work since a whole page(256bits) needs to be written at once. Maybe I can upgrade this later with a more decent flash chip, which will allow easy writing just like the ram.

JMP(C/Z)-instructions
Since the jmp instructions do not support offset but only immediate operands, the compiler needs to make sure that if a target of a jmp is not in the current 256byte block, a FAR_JMP with both high and low address are emmitted.

Instructions
Instruction Nibble 1
Nibble 1	Instruction	Note	Cycles	Notes	Decode Table / A,B or C
0x0	ADD reg1, reg2	reg1+ reg2. result is in reg1		Sets the carry flag if overflow occures / clears if not	A
0x1	SUB reg1, reg2	reg1-reg2. Result is in reg1		To be tested!	A
0x2	NOR reg1, reg2	Logic NOR. Result in reg1			A
0x3	AND reg1, reg2	Logic AND. Result in reg1			A
0x4	MOV reg1,reg2	Mov reg2 int reg1. Reg2 can be a number!			A
0x5	MOVZ reg1, reg2	Same as mov. executes only when reg1 is zero		Do we need a flipflop for REG1_ZERO_MOVZ, if reg1 is changed during a MOVZ instruction, which in turn could have an effect on the STATE_SIGNAL of the / MOV instruction?	A
0x6	JMP reg1, reg2	Far jump(needed when jumping over 127 bytes) reg1 is LOW byte, reg2 HIGH byte, reg2 can be a nr		If the JMP has only one argument, it is used as an offset instead as an address. the Carry(MOVC)	A / 0x00 is pc_high, number
0x7	JMPZ reg1, reg2	Same as JMP, executes only when reg1 is zero		Opreand 0x00 is: / pc_high, number	A
0x8	JMPC reg1, reg2	Same as JMP, executes only when carry is set		Opreand 0x00 is: / pc_high, number	A
0x9	STR reg1	Store reg1 at BR			C
0xA	LDA reg1	Load value pointed to by BR into reg1			B
0xB	SET_BR reg1, reg2	Set BR_HIGH to reg1, BR_LOW to reg2			A
0xC
0xD	COUNT_BR UP / or / COUNT_BR DOWN	Increment / or / Decrement i16(BR)			none
0xE	PUSH reg1	Simple fifo in seperated Memory			C
0xF	POP reg1	Simple FIFO in seperated Memory			B

Argument decode Table A
 The second instruction Nibble defines the operand registers.
Table A is used by MOV, ALU, SET_BR and ALU

Opcode Nibble 2	Involved Registers
0x0	Reg1,number	JMP(Z/C) uses this operand byte to encode / JMP(Z/C) pc_high, number / thus JMP(Z/C) reg1, number cant be used.
0x1	Reg2, number
0x2	Reg3, number
0x3	Reg4, number
0x4	Reg1, reg2
0x5	Reg1, reg3
0x6	Reg1, reg4
0x7	Reg2, reg1
0x8	Reg2, reg3
0x9	Reg2, reg4
0xA	Reg3, reg1
0xB	Reg3, reg2
0xC	Reg3, reg4
0xD	Reg4, reg1
0xE	Reg4, Reg2
0xF	Reg4, Reg3

Argument Input Table B
Used by LDA and POP

Opcode Nibble 2	Involved Registers
0x0	Reg1
0x1	Reg2
0x2	Reg3
0x3	Reg4
0x4	BR_LOW
0x5	BR_HIGH
0x6	IO_Output_Register_1
0x7	IO_Output_Register_2

Argument Output Table C
Used by STR and PUSH

Opcode Nibble 2	Involved Registers
0x0	Reg1
0x1	Reg2
0x2	Reg3
0x3	Reg4
0x4	Number
0x5	BR_LOW
0x6	BR_HIGH
0x7	IO_Input_Register_1	What to put here?

Calling Convention
-Caller saves his working registers(For example on the stack)
-Arguments are passed in Reg1, Reg2, Reg3. Additional arguments are passed via the stack(Reg4 cannot be used since it is needed for the call)
-Return Address is passed through the stack. First the Low byte is pushed, than the High byte
-Return values are in Reg1 and Reg2. Additional return values are on the stack (Reg3 and 4 cannot be used since they are needed for the return JMP instruction)

Hardware Implementation

The 74HCT logic family is used. Write here the propagation delay calculation, Power consumption, and performance charachteristics.
PC and SP are implemented using 74xx193 binary counters. With that no 16 bit addition needs to be done

Accessing Memory
Step	Read	Write
1	Apply address to A-bus, clear Not_OE and NOT_CS	Apply address to A-bus, Apply data to D-bus, clear Not_OE and NOT_CS
2	wait > 6nS	wait > 6nS
3	Read Data from Databus / Write read data back to registers	Set NotCS
4	Set NotCS

Fetch and Decode
Step	Fetch and Decode
1	Connect PC to Mem Addr, IR to DBus
2	Do Mem Read and IR write Signals
3	Connect PC and 1(through multiplexer ctrl)to ALU, ADD ctrl
4	Reg write back

Execution steps
Command/Cycle	1	2	3	4	5
ALU	Write REG A to dbus / High to low triggered	Latch Reg A from the dbus for the ALU. / Since this happens at the High to low transition, it cant be done earlier	Write REG B to dbus	At the High-To-Low transition of the state signal the ALU-Output is latched	Fill register
MOV(Z)	Write REG to DBus	Fill REGs
LDA
STR
JMP(C/Z)	Write regA to DBUS	Fill pc_low with reg / if reg0 is 0x00 done	Apply RegB to dbus / This is done using the multiplexer to use an input selector as an output selector	Fill pc_high with reg2
COUNT_BR	Increment/Decrement BR
PUSH	Decrement SP
POP			Increment SP
SET_BR	Write reg to DBUS	Fill pc_low with reg	Apply the Table 2 multiplexer that decode Table 2 is used	Fill br with reg2

Current Problems

MOV, PUSH, POP, JMP etc.. need implementation for second fetch!

ALU carry_out signal is changed by NOR and AND instructions. Need a flip Flop or something similar

PROBLEMS
Startup
RING_CNTR_CLR needs to go high -> this clears the Ring Counter. Is this signal low active?
Further investigation is needed!
CLR_ALL_REGS_NOT needs to go low for a short period and then for the rest of the time HIGH
Memory Access
-Read: can we apply the address, clear_not_oe and clear_not_cs in one istruction and fill the registers in the following instruction? 2Cycle Memory Access would be possible with this!

How to initialize the registers when power is turned on???